## Slide 1: INTRODUCTION TO NEONATAL MECHANICAL VENTILATION
CHU Ste-Justine
CHU Ste-Justine

## Slide 2: Adapted objectives
Terminology drowned in synonyms
Learning according to the parameters:
  FiO2, PEEP, PIP, ΔP, Frequency and Inspiratory assistance
Physiology and basic principles
  Neonatal ventilation
No pathology or prolonged ventilation
4

## Slide 3: Plan
5
Physiology
Non-invasive ventilation
Conventional ventilation
High-frequency oscillatory ventilation
Weaning from ventilation (for RDS)

## Slide 4: Respiratory physiology
6
Respiratory center
Responds to CO2 > pH > O2

## Slide 5: Respiratory physiology – spiro
0
15
30
37
80
Volume (mL/Kg)
7
Tidal volume
Functional residual capacity

## Slide 6: Respiratory physiology
8
Pulmonary compliance
Δvolume with Δpressure
Static (Pplateau)
peak
Dynamic (P )
V 
P
VT
P[ plat|crête]  PEP

## Slide 7: Types of ventilation
Non-invasive ventilation (mask, nasal prongs, nasal CPAP)
  1 or 2 pressure levels
  High-flow nasal cannula (HFNC)
Invasive ventilation (ETT, tracheostomy)
  Conventional: barometric / volumetric
  Non conventional
    High-frequency oscillation
    Others: Hayek, ECMO, etc.
9

## Slide 8: Non-invasive ventilation
10
http://perlbal.hi-pi.com/blog-images/216823/gd/1220960127.jpg

## Slide 9: NIV – CPAP
Guarantee a minimum pressure in the pulmonary tree
Alveolar recruitment
Increases functional residual capacity
  Promotes gas exchange (O2 > CO2)
1.
Shaffer, T.H., et al., Neonatal non-invasive respiratory support: physiological implications. Pediatr Pulmonol, 2012. 47(9): p. 837-47
11

## Slide 10: NIV – CPAP
↓ pulmonary edema
Support for the work of the left ventricle
Neonatal specificities1:
  Thoracic stability
  Stimulation of surfactant synthesis
1. Shaffer, T.H., et al., Neonatal non-invasive respiratory support: physiological implications. Pediatr Pulmonol, 2012. 47(9): p. 837-47
12

## Slide 11: Impact on cardiac work (LV)
Spontaneous
Mechanical
13
1.
Lacroix, J., et al., Urgences et soins intensifs pédiatriques. 2nd ed. 2007: Masson. 1368 p.
+15
60
80
-15
95
80

## Slide 12: NIV – PEEP and compliance [adult]
14
Adult values

## Slide 13: HHHFNC (High-flow nasal cannula)
Variable, humidified and heated FiO2
Constant flow, but variable PEEP
  ≈ 6 cmH2O with « massive intra- and interpatient variability » 1
  Max 6±1 cmH2O with 8 L/min2
Possible washing of the nasopharyngeal dead space
Risks low
16

## Slide 14: NIV – nIPPV
Biphasic ventilation (Bi-level positive airway pressure)
  1 PEEP level + 1 inspiratory assist level
  ± frequency
Problematic synchronization
  Facial mask seal required or NAVA
Valves (inspiratory and expiratory) open
BiPAP™ ≠ BIPAP ≠ BIPAPEvita™
17

## Slide 15: NIV – nIPPV
18
1
2
3
4
5
6
time
P
cmH2O
PC
BPAP

## Slide 16: NIV – BPAP
Benefits
  Benefits of CPAP + ↓ respiratory work
  Preventative of intubation1
  Preventative of neonatal re-intubation2 (vs CPAP)
Risks
  Barotrauma
  Inappropriate use (age, state of consciousness, etc.)
19

## Slide 17: Conventional ventilation
20
http://kadiera.quicksilverdragon.com/gallery2/d/140-2/p6130500.jpg
Not normal

## Slide 18: Conventional ventilation
FiO2 and PEEP
PIP (=Pinspiration =Plimit, =Pmax, =Ppeak)
Tidal volume
Minimum respiratory rate
Type of assistance (“breathing surplus”)
  With inspiratory assistance [sIMV-Ai] or without [sIMV]
Inspiratory time (or I:E ratio)
Alarms and flow thresholds
21

## Slide 19: Barometric ventilation
22
Volume
Pressure oriented
Time
Pressure
Flow-phase
Pause- phase
Inspiration
Expiration
Flow-phase
Time
Pause- phase

## Slide 20: Conventional ventilation
23
Pressure
Time
Flow
Time
Time
Inspiration
Expiration
Pause-
Flow-phase phase
Pressure
Flow
Volume
Pressure oriented
Pause-
Flow-phase phase Flow-phase
Inspiration Expiration
Time
Time
Time
Pause- phase

## Slide 21: Ventilation – lexicon
ACV:
Assisted controlled ventilation
Each breath is supported identically Usable in barometric or volumetric mode
sIMV-PSV: Intermittent VAC
Additional breaths with PSV
"Guaranteed” volume
VG:
(= VCRP,
=PRVC)
Inspiratory pressure adjusted according to a target volume Barometric mode, even if a volume is set
25

## Slide 22: Ventilation – ventilators
26
Sechrist
Babylog 8000

## Slide 23: Ventilation – ventilators
27
Evita XL
InfantFlow (NIV only)

## Slide 24: Ventilation – ventilators
28
VN500
Servo-i

## Slide 25: Ventilation – summary
1.
Lacroix, J., et al., Urgences et soins intensifs pédiatriques. 2nd ed. 2007: Masson. 1368 p.
29
VT
TI
Frequency
Ratio I/E
TE
Pmax
PEEP
Instantaneous flow
Pavg
FiO2
CO2
Ventilation
O2
Oxygenation

## Slide 26: Conventional vent weaning
30

## Slide 27: Weaning
Depends on the mode chosen and
  Child's age
  Underlying pathology
  Duration of ventilation
Overall principle:
  Lower the support with the goal of extubation
Possible to extubate from HFOV
31

## Slide 28: Criteria
Spontaneous respiratory rate (neuro, sedation)
No airway obstruction
  Before intubation or after (s-glottic stenosis)
Sufficient neurological status
  Spontaneous RR, secretion management
Stable hemodynamics
  Reinversion of thoracic pressures
32

## Slide 29: Criteria – parameters
No consensus, many variables
Alternatives (BPAP, LNHD) constantly evolving Less high step for patients
Probably:
  PEEP < 7 with FiO2 < 50%
  PIP < 25
33

## Slide 30: HMD weaning
34
Reliable PTCCO2, FiO2 <40%
Guarantee PEEP at all times
Volumetric sIMV mode
Maintain Vt 4-5 mL/kg, MV/kg 240-360 mL/min/kg
Decrease PEEP to 5 cmH2O; if FiO2 ≤ 30%, decrease PEEP to 4 cmH2O
If Al: set Al to 50% of ΔP, decrease Al by 1-2 cmH2O every 2 hours to 5 cmH2O
Decrease RR by 10/min every 1-2 hours to RR 20/min, according to astrup or PtcCO2 45-55 mmHg
Inform the doctor that the patient is ready for extubation if PIP is between 12-16 cmH20
Barometric sIMV mode
Decrease PIP by 1-2 cmH2O every 2 hours to 12-16 cmH2O
Maintain Vt 4-5 mL/kg, MV/kg 240-360 mL/min/kg
Decrease PEEP to 5 cmH2O; if FiO2 ≤ 30%, decrease PEEP to 4 cmH2O
If Al: set Al to 50% of ΔP, decrease Al by 1-2 cmH2O every 2 hours to 5 cmH2O
Decrease RR by 10/min every 1-2 hours to RR 20/min, according to astrup or PtcCO2 45-55 mmHg
Inform the doctor that the patient is ready for extubation

## Slide 31: Extubation <28 weeks <1000g
In summary:
PEEP at all times
Caffeine
No bath, minimize care
Great surveillance
35

## Slide 32: High-frequency
36

## Slide 33: High frequency ventilation
VT less than dead space Frequency > 60/min (>1 Hz)
4 different types:
  Oscillations: most used (and the only one available HSJ)
  Jet: very specific (ENT, emergency crico)
  Positive pressure: abandoned
  Percussion: mixed mode, few studies
37

## Slide 34: HFOV – Main principles
38
Low-Pass Filter
Lung
Fresh Gas Bias Flow
Piston Pump
Taylor principle
By piston (SensorMedic™)

## Slide 35: HFOV – Main principles
* Adult scale
39

## Slide 36: The magic of oscillation
40

## Slide 37: HFOV – indications
Early vs late
  Multiple studies in babies, no advantage o early HFOV
  Pediatric indication in sharp decline
    Almost obsolete in adults
Particularly effective: (i.e: avoids ECMO)
  Meconium pneumonitis
41

## Slide 38: HFOV – device
42

## Slide 39: Adjust the HFOV
MAP: action on oxygenation especially
  Adjustment according to CXR and SpO2, be careful of overdistension
Amplitude
  Obtain a visible chest vibration
  Adjust according to PCO2
Guaranteed volume
  About 2 mL/Kg
  Monitor the amplitudes generated
43

## Slide 40: Adjust HFOV – frequency
Frequency
  Initial: high frequency (10 Hz)
  Adjustment only if you absolutely have to
    Volumetric: ↑frequency, ↑ventilation
    Barometric, it's the opposite…
  ETT size
44

## Slide 41: HFOV – frequency
1. Effect of frequency on tidal volume (∫flow)
45
1
2
3
4
5
6
time
Flow
mL/s

## Slide 42: Weaning from HFOV
Spontaneous breathing rate
No airway obstruction
  Present before intubation or after (s-glottic stenosis)
  Secretion management
Sufficient neurological status
Stable hemodynamics
  Reinversion of thoracic pressures
48

## Slide 43: Ventilation – usual parameters
50
PEEP:
PIP:
TV:
Resp rate:
4-8 cmH2O
10-30 cmH2O
4-6 mL/Kg
normal for age
Inspiratory assist: 5-10 cmH2O or 50% ΔP
FiO2:
Ti (or I:E ratio)
According to SpO2
According to TV and frequency

## Slide 44: VHFO – usual parameters
Average pressure:
Amplitude: Guaranteed volume:
Frequency:
Inspi:Expi Ratio
10-18 cmH2O
Pmean conv. + 2-4 cmH2O
≈8 intercostal spaces
10-35 cmH2O (chest vibration)
≈ 2 mL/Kg (?)
8-12 Hz
1:2 (33%)
51

## Slide 45: Thank you for your attention
52