## Slide 1
Patient assessment

## Slide 2: Neonatal ventilation
Respiratory assessment
 | 0 | 1 | 2
Nasal flaring | None | Moderate (+) | Marked (++)
Expiratory grunt | None | Audible with stethoscope | Audible to the ear
Xiphoid retraction | None | Moderate (+) | Marked (++)
Chest movement | Synchronized with the abdomen | Slight asynchrony | Marked asynchrony, Thoracoabdominal rocking See-Saw
Intercostal retraction | Absent | Moderate (+) | Marked (++)
Notes: Toujours l’examen physique en premier!!!!!
Pourquoi le tirage sous costal n’en fait pas partie?
Normal en contexte de DBP
Respiration abdominale chez le bébé

## Slide 3: Why the silverman score
Hedstrom, A. B., Gove, N. E., Mayock, D. E. & Batra, M. Performance of the Silverman Andersen Respiratory Severity Score in predicting PCO2 and respiratory support in newborns: a prospective cohort study. J Perinatol 38, 505–511 (2018).

## Slide 4: Neonatal ventilation
Administer surfactant…..
        Although – LISA
Apnea of prematurity…..
        Although – Caffeine,
ENT abnormalities
Central or neuromuscular problems
Sedation/pain relief
Respiratory failure
Why?

## Slide 5: Indications
Either based on clinical presentation
Or
Blood gas results
Or
Difficulties with oxygenation

## Slide 6: Indications
Either based on clinical presentation
  EG Silverman score >6
Or
Blood gas results
  EG acute PCO2>65
Or
Difficulties with oxygenation
  EG, more than 75% FiO2 on CPAP at 8 cmH2O

## Slide 7
Basic terms

## Slide 8: Basic terms
Pressure
Time
PEEP
∆P
Ppeak
Or
PIP
Ti
Te

## Slide 9: Basic terms
Volume
Time
Inspired volume
Expired volume
Ti
Te

## Slide 10: Basic terms
Pressure
Volume
Ppeak
Ti

## Slide 11
Invasive ventilation

## Slide 12
Conventional ventilation

## Slide 13: nomenclature
Volumetric ventilation
Assist/control ventilation (VAC)
      PC-VAC-VG
Intermittent assisted controlled ventilation (VACi)
  Or called Synchronized Intermittent Mandatory Ventilation (SIMV)
Barometric ventilation
Assist/control ventilation (VAC)
      PC-VAC
Intermittent assisted controlled ventilation (VACi)
  Or called Synchronized Intermittent Mandatory Ventilation (SIMV)
Pressure Support

## Slide 14: Oxygenation
PaO2 is increased by increases in mean airway pressure
This is true in any low volume, atelectatic lung disease.
And not true in other diseases!
Because of improved V/Q matching.
  Above a certain point increases in mean airway pressure may lead to decreases in cardiac output, even though PaO2 continues to increase.
  This point depends on the stiffness of the lungs

## Slide 15
PaO2
Mean Airway Pressure
O2 delivery
Cardiac Output

## Slide 16: Oxygenation
The mean airway pressure is the average airway pressure over one minute.
The mean airway pressure can be increased by
  Increasing PEEP
  Increasing pip
  Lengthening inspiratory time (Ti)
  Shortening expiratory time (Te)
  Increasing the flow rate will increase how fast you get up to the peak pressure, so achieves more of a “square wave”.

## Slide 17: Oxygenation
Effects of those changes on Oxygenation are not identical
Eficacity of Peep > pip > increasing Ti >changing flow rate
Come back to this later

## Slide 18: CO2 Removal
VCO2 a VA (minute alveolar ventilation)
VA = (RR x Vd-Vt)
Therefore increasing respiratory rate, or increasing tidal volume, or decreasing dead space will increase CO2 removal.
If expiratory time gets too short, then tidal volume will fall, due to lack of sufficient time for the lungs to empty.
Thus there is a limit to how fast you can go with conventional ventilation

## Slide 19: CO2 removal
The lungs empty passively based on the static recoil of the lung and chest wall system, and on the resistance to airflow of the airways.
Need to have time to exhale
Otherwise, even with a faster rate, gas trapping and reduced tidal volue and less CO2 removal

## Slide 20: Patient interaction with the ventilator
Five patterns described
  Apnea
  Asynchrony
  Synchrony
  Active expiration against ventilator inflation.
We now always use synchronized ventilation so No 2 no longer occurs. (as long as it is working!)
If Ti is too long, the babies can begin to expire against the vent.

## Slide 21: Modes of ventilation used
SIMV
A/C
  Can be purely pressure, or ‘volume guaranteed’
HFV
  Oscillator
  Jet

## Slide 22: IMV
Neonatal ventilators all have continuous flow through the circuit to allow the infant to breathe spontaneously at any time.
This flow can be in a pressurized circuit, to give CPAP
This continuous positive pressure is supplemented by cyclic elevations in circuit pressure to a higher level, the peak inspiratory pressure.
Traditionally the pressures have been cycled on a strict temporal basis.
This is “pressure limited time cycled” ventilation

## Slide 23: SIMV
Ventilators detect neonatal respiratory efforts.
They use either changes in pressure or flow in the circuit to trigger the ventilator to deliver a positive pressure breath with a preset pressure and duration.
The duration of expiration therefore varies.
The number of positive pressure breaths is set by the operator.
If the infant is apneic they will still receive the set, minimum number of breaths.
If the patient breathes faster than the set rate, they still get the same number of positive pressure breaths.

## Slide 24: Assist control
Assist control is another mode of triggered ventilation whereby the minimum number of breaths is set by the operator
If the infant is breathing faster than the set rate then the ventilator will deliver more breaths.
The limit is usually determined by the logic in the software and can potentially lead to very short expiratory times.
Some ventilators have no upper limit and can deliver up to 150 breaths per minute leaving little time for expiration

## Slide 25: SIMV, A/C
The baby is breathing at a rate of 70
You change the ventilator set rate from 30 to 40 this will have very different effects for SIMV vs A/C, (assume a set inspiratory time of 0.5 sec.)
SIMV, the number of positive pressure breaths will increase from 30 to 40. The expiratory time will decrease from an average of 1.5 to 1.0 (varies from breath to breath)
  The remaining 40 or 30 breaths can either be unsupported, or can trigger a PSV breath
A/C, the number of positive pressure breaths will be unchanged at 70. The expiratory time is unchanged at an average of .36 seconds (varies from breath to breath).

## Slide 26: Conventional ventilation
 | PC-VAC-VG | PC-VAC | PC-VACI-VG | PC-VACI
Pressure | Variable ad Pmax | Fixed | Variable on the VG, fixed on the Ai | Fixed on the frequency and fixed on the Ai
Volume | Fixed | Variable | Fixed frequency, variable on the Ai | Variable
Ti | Fixed | Fixed | Fixed on the frequency, Variable on the Ai | Fixed on the frequency, Variable on the Ai
Type of support | All breaths supported in the same way | All breaths supported in the same way | All breaths on the rate are supported in the same way Breaths beyond the rate are supported with pressure support | All breaths on the rate are supported in the same way Breaths beyond the rate are supported with pressure support
Pressure support | No | No | Yes | Yes
PEP | Yes | Yes | Yes | Yes
Frequency | Yes | Yes | Yes | Yes
Basics
Notes: Le choix devrait être basé
1- sur les fuites : si fuites <40%, pas de raison de mettre en pression
2- AG: si préma: pas de raison de mettre en VACI – perd complètement l’avantage de la ventilation en volume

## Slide 27: Conventional ventilation
 | PC-VAC-VG | PC-VAC | PC-VACI-VG | PC-VACI
Pressure | PMax | Fixed | VG : Pmax Fixed on the Ai | Fixed
Volume | Variable-target set by clinician Limit of 130% of the target | Variable – no limit | Fixed frequency, Variable on the Ai – No limit The fan will ring | Variable – No limit The fan will ring
Frequency | Yes Alarm based on Ti/Te | Yes Alarm based on Ti/Te | Yes | Yes
Security
Difference between PLimit and PMax

## Slide 28
Why volume ventilation?
Notes: Actuellement pas de données montrant une supériorité de la ventilation par haute fréquence vs la ventilation conventionnelle.
Volumétrique:
Volume courant cible 4-6 ml/kg (souvent un peu plus grand chez les extrêmes prémas vu l’espace mort) 1-5
Réduction de la DBP
  Donc, ne fait pas de sens d’utiliser le VACi
  Pas de raison de mettre en pression
    Sauf: pas extubable ET bébé ne génère pas de volumes plus grand ET gaz anormal sans possibilité d’améliorer la ventilation

## Slide 29: Assisted ventilation in neonates
Historically
  Modified Ayre’s t-piece
  Continuous flow in the circuit
  Baby can inhale at any time
Now
  Inhalation triggered by the child: usually by an inspiratory flow (with flowmeter)
      Possible alternative triggered by pressure reduction
  Duration of inhalation determined by us (VAC)
  Duration of inhalation determined by inspiratory flow (AI)
    Inspiration ends when inspiratory flow decreases to 25% of maximum flow (or other %)

## Slide 32: Synchronized ventilation
Even with VAC
Child may begin to exhale against the ventilator's inhalation
Especially when the Ti is too long
Increases risk of pneumothorax

## Slide 33
Active expiration against ventilator
Frequent if Ti >0.3 s
Infrequent if Ti<0.2

## Slide 34: Pulmonary diseases of small volumes
Increase in MAP increases oxygenation
    Increases SpO2/FiO2 without impact on cardiac output
    Oxygenation = SpO2 x HgB x Cardiac output
  MMH
  Pneumonia
  ARDS
  Few cases of MAS
But NOT for Hypoplastic Lungs
  Increase in MAP decreases Cardiac output without direct impact on SpO2
Or for diseases with normal or increased volumes
  Some cases of MAS have more « air-trapping »

## Slide 35
The impacts of increasing MAP on oxygenation depend on the option taken
For the same increase in MAP,
PEEP > pip >Ti

## Slide 36: Expiration
Normally, exhalation is passive Determined by: Elastic recoil pressure Expired exchange, based on compliance Pulmonary resistance Airway resistance (especially), and tissues Healthy term NN, reduced compliance, normal resistance NN preterm MMH, very low compliance, normal strength Intubated NN MMH, very low compliance, increased resistance NN DBP, low compliance, increased resistance

## Slide 37: Expiration
Exhalation force is the elastic recoil pressure, = compliance Resistance delays expiration Expiration is logarithmic

## Slide 39: Time constant
τ RS = RxC
Typical compliance = 1.0 normal lungs: = 0.1 for HMD ( mL /cmH2O/kg)
Typical resistance = 100 -300 for ETT 2.5, 50 -150 for 3.0 (cmH2O/L/s)
Time constant = 0.1 - 0.3 s normal lungs,
0.01 -0.05 for HMD

## Slide 40: ETT resistance
Even if we're talking about physiology…

## Slide 41: Te (assisted breathing)
Te must be > 3 times τRS
VAC, If child is tachypneic and Ti is too long, it is possible that Te would be <3τRS
Possibility of gas trapping, especially with normal compliance
Unlikely with HMD
  Reduced compliance - very low τRS
BPD, high resistance, longer τRS, prolonged expiration required.

## Slide 42: Volumetric
When the baby does not breathe, the pressure and volume modes are identical
The ventilation mode has no impact on lung mechanics
If we switch from pressure to volume and the peak pressures rise, it's because the volumes have also increased.
Volume ventilation:
  safety factor (absent in barometric)
  if Vt > 130% of desired volume, valves open, Paw drops to PEEP,
    We set a Ptp limit

## Slide 43: Volumetric?
No volume-controlled ventilation in neonates
Targeted volume ventilation
Same inhalation production mechanism
Pressure varies according to integrated algorithm, pip adjusted to reach desired volume
If baby does not breathe, it takes around 3 inhalations to get there
If sudden compliance change
3 inhalations for new Ppeak

## Slide 45
Several very large inspirations = very high Ptp
Several terminated inspirations = Vt>130% VG
Low and stable Ptp

## Slide 46: Volume ventilation
23
Volume Guaranti started, Vt 3mL
Volume Guaranti closed
Ventilated 17/6,
Vt around 2.3 mL
Ppeak rises up to 24
Vt much more variable in pressure mode, minute volume drops from 0.2 liters to 0.16

## Slide 47
Two algorithms running continuously
One for triggered inhalation, the other for controlled inhalation (UT, untriggered)

## Slide 48: Volume ventilation
When the baby breathes well
Sometimes the Ppeak drops and there is little « delta-P »
This happens because the child is receiving adequate volumes, so it is not necessarily a problem
There is only a problem if the baby still needs a higher average pressure for its VQ « matching », and the FiO2 rises
If the FiO2 rises, the most logical response is to increase the PEEP
Rather than changing to barometric
If the FiO2 does not rise… extubate

## Slide 53: Preventing Atelectasis
Requires adequate PEEP
  varies by patient, depending on static compliance
Adequate tidal volume
  Less variable but pressures required very variable
What is the right tidal volume?
  Probably between 3 and 6 mL/kg
  Normal physiologic Vt lies between 3 and 8 mL/kg

## Slide 54: Ventilator Parameters
Volume ventilation mode (VGV or volume control)
4 to 5 mL/kg (or 4 mL/kg plus 0.5 mL for the ETT)
If in more than 21% O2: PEEP of 5 to 8 before surfactant, increase PEEP to keep FiO2 less than 60%
Surfactant as early as possible
After surfactant reduce PEEP to 4 if in 21% O2, if remains in 21% reduce to 3, if remains in 21%, WEAN.

## Slide 55
A potential useful application of ventilator graphics

## Slide 56: Ventilator paramteres
What are you going to wean, and what are you going to monitor?
If on an SIMV mode, wean rate, but if your ventilator gives PSV then you are switching to pressure ventilation….
If on an A/C mode watch pressures and spontaneous rate, reduce the back up rate progressively (maybe) and extubate when the pip is below a certain thershold.
What to do about CO2?

## Slide 57: Permissive hypercapnia
Increasing ventilation to normalize a CO2 risks increasing lung injury for questionable benefit
Permissive hypercapnia does not mean forcing the CO2 to increase!!
It means not chasing the CO2 if the tidal volume is OK, the FiO2 is OK and the baby is clinically OK
It means being prepared to wean the vent if all those factors are OK, even in the face of elevated CO2
But is there a limit?

## Slide 58: Early extubation
Removing the tube as fast as appropriate
Or not intubating if you can avoid it
Self-evident that never being ventilated is better than being ventilated (BPD does occur in never intubated babies, but only mild forms)
But if you need surfactant: the sooner the better, even an hour of delay makes a difference
The challenge to identify quickly infants who will need surfactant

## Slide 59: Improving the success of early extubation
Caffeine

## Slide 60: 3 questions
When we give surfactant, what happens to lung compliance?
If we decrease the PEEP and Pl by 2 each, what happens to the tidal volume?
If we put a child on volume ventilation, and we give surfactant, will there be an « automatic » weaning?

## Slide 61: Effects of Surfactant on dynamic compliance
 | Surfactant |  | Control | 
 | Before | After | Before | After
Compliance (ml/cm H20/kg) | 0.43 _+ 0.21 | 0.45 _+ 0.45 | 0.33 _+ 0.14 | 0.33 ___ 0.13
Resistance (cm H20/L/sec) | 141 _+ 90 | 175 _+ 97 | 160 _+ 90 | 173 + 98
Tidal volume (ml/kg) | 6.3 _+ 1.7 | 5.3 _+ 1.5 | 6.9 _+ 2.1 | 6.0 + 1.9
Table II. Combined pulmonary mechanics data
Values are expressed as mean _+ SD.
Immediately before and 1 hour after
Couser, R., T. Ferrara, et al. (1990). "Effects of exogenous surfactant therapy on dynamic compliance during mechanical breathing in preterm infants with hyaline membrane disease." The Journal of Pediatrics 116(1): 119-124.

## Slide 62
STATIC PRESSURE-VOLUME CURVE

## Slide 63: Effects of surfactant

## Slide 64: Goldsmith LS et al. Immediate Improvement in Lung Volume After Exogenous Surfactant: Alveolar Recruitment Versus Increased Distention. The Journal of pediatrics. 1991;119:424.

## Slide 66: Static Compliance
Stenson, B. J., R. M. Glover, et al. (1994). "Static respiratory compliance in the newborn. III: Early changes after exogenous surfactant treatment." Arch Dis Child Fetal Neonatal Ed 70(1): F19-24.

## Slide 67: 3 questions
When you give surfactant, what happens to pulmonary compliance?
If we decrease the PEEP and the PIP by 2 each, what happens to the tidal volume?
If we put a child on volume ventilation, and we give surfactant, will there be an "automatic" weaning?

## Slide 69: 3 questions
When you give surfactant, what happens to pulmonary compliance?
If we decrease the PEEP and the PIP by 2 each, what happens to the tidal volume?
If we put a child on volume ventilation, and we give surfactant, will there be an "automatic" weaning?

## Slide 70: Volume ventilation and surfactant
If the PEEP is not reduced, there will not necessarily be a reduction in Peak pressure.
On the other hand, a reduction of PEEP by 1 cmH2O often leads to a much larger reduction in Peak pressures.
If we ventilate by pressure, a reduction of PEEP and PIP by 4, can greatly increase volumes

## Slide 71
We cannot use the graphs to determine if the PEEP is optimal or if the baby is ready for weaning
Look at the FiO2
When the FiO2 drops, reduce the PEEP. We will see that the Peak pressure drops (volumetric) or the volume increases (barometric)
If at 21% after surfactant, PEEP can be reduced to 3 cmH2O,
    Dimitriou, G., A. Greenough, et al. (1999). "Appropriate positive end expiratory pressure level in surfactant-treated preterm infants." Eur J Pediatr 158: 888-891.
    at 4 and 5 cmH2O they were over-distended.
Or at 2 cmH2O,
    Sandberg K et al, 2007. Pediatr Res
    overdistension even at 4 cmH2O

## Slide 72: Prevention of over-distension
  Prevent excessive expiratory volumes
  Prevent excessive tidal volumes

## Slide 73: Lung damage
Over-distension more important than too much pressure
Tracheal pressures little impact if over-distension is avoided
  Several animal studies demonstrate that reduced mobility of the rib cages eliminates the effects of very high pressure.
  If the tidal volumes remain normal, no barotrauma
How can we know if there is over-distension?

## Slide 74: Reduction of over-distension
Graphs on the ventilator?
No data that they are useful for limiting lung damage
Why not?
  Leaks
  Dynamic not Static
  Change with each breath

## Slide 75
Pressure-volume loops.
Donn S M , Sinha S K Arch Dis Child Fetal Neonatal Ed 2006;91:F226-F230
Pressure-volume loops. (A) The loop shows hyperinflation, with an upper inflection point on the inspiratory limb. (B) The loop has been normalised by reducing the peak inspiratory pressure. Vt, Tidal volume; Paw, peak airways pressure.
Notes: Pressure-volume loops. (A) The loop shows hyperinflation, with an upper inflection point on the inspiratory limb. (B) The loop has been normalised by reducing the peak inspiratory pressure. Vt, Tidal volume; Paw, peak airways pressure.

## Slide 77: Overdistension
Due to leaks and volume variability, the ventilation graphs return to zero at the end of expiration.
It is impossible to know the pulmonary volume at the end of expiration, or even if there has been a change,
  methods exist; but research

## Slide 79: Animal models
Prevention of over-distension avoids pulmonary damage
If there is restriction of the rib cage, tracheal pressure rises during inhalation (PPV), intrapleural pressure also rises, less transpulmonary pressure
Physiological situation: correlation between administered pressure and tidal volume for apneic patient

## Slide 80: To avoid pulmonary damage
Reduction of overdistension
  Optimal PEEP
  Optimal tidal volume
Prevention of atelectasis
Intubation only when necessary
Give surfactant immediately when required
Prevention of infections

## Slide 81: Conventional ventilation
Optimal PEEP?
  Difficult to determine in the newborn
  Low FiO2 21-23% = try to decrease the PEEP
  Oxygenation improved with higher PEEP only if recruitable disease
  Risks
      Decreased venous return
      Increased shunt
      Increased lung damage
      Decreased oxygenation
      Decreased cardiac function
        When in doubt – Lung X-ray helps a little
Parameters

## Slide 82: Conventional ventilation
Volume:
  Target 4-6 ml/kg
  Contribution of dead space
      The smaller the baby, the more volume it needs
      Some centers use 4 mL/kg plus 0.5 mL for the EM
parameters

## Slide 83: Conventional ventilation
Barometric/Pressure (Delta-P):
  To be used ONLY in the presence of >40% leaks
  Delta-Pressure required to have a satisfactory gas – the volume is no longer reliable due to the leaks
parameters

## Slide 84: Conventional ventilation
Frequency/Ti:
  Start at 50/min.
  Ti: At the discretion of the resp. therapist, re-evaluate at each shift to promote recruitment without causing air tapping.
  Ensure Ti<0.3s if baby is breathing
parameters

## Slide 85: Conventional ventilation
Ai:
  Pressure ventilation mode
    Variable Ti depending on inspiratory flow
    Inhalation ends when inspi flow <25% of max
  To be used only in conscious term infants without risk of pulmonary disease (Cooling, Tachypneic Pt)
  May allow more comfort
parameters

## Slide 86: Conventional ventilation
PEEP: Consider the possibility of malacia
Volume: Often requires larger volumes (may exceed 6 mL/kg)
Frequency: Low (30-40/min.)
Ti: longer (be careful of inverted ratio)
Requires a long Te
Approach to severe BPD
Notes: Quels sont les signes de malacie?
Début de vie:
Système respiratoire relativement uniforme
Short time constant
Fréquence plus haute avec Ti courts
Petits volumes
DBP sévère établie
Système respiratoire hétérogène
Résistances différentes
Faible fréquence (le plus bas possible si le bébé ne veut pas être tachypnéique), Ti longs
Grand volumes
Croissance!!!!!! – peuvent nécessiter jusqu’à >130 kcal/kg/jour, par contre on vise une bonne croissance staturo-pondérale, le poids n’est pas un bon indicateur seul! – PROTÉINES!!! – apports liquidiens plus bas, avec de bonnes calories

## Slide 87
Situation:
I'm calling you because baby X no longer has Delta-P, “it should be put on pressure”
Notes: Quelle est votre réponse?
Qu’est-ce qui DOIT être évalué?
Examen physique – est-ce que le bébé a beaucoup de détresse respiratoire?
Besoins en O2 – pareils ou augmentés
TRS +/- extubation – est-ce que le bébé est extubable?
Volumes générés – est-ce que le bébé génère des volumes + grands que ceux réglés? Si oui, c’est le volume qu’il faut augmenter
Gaz – est-ce que le dernier gaz était bien, de quand date le dernier gaz?
Décision doit être rapide, tendances, évaluation au chevet

## Slide 88
High frequency ventilation
Notes: VN500 ou SM3100

## Slide 89: Basic terms
Amplitude
Time
A
I : E
Volume

## Slide 90: High frequency ventilation
Indication:
  Persistent respiratory acidosis (<7.2 with pCO2>60)
      With frequency >60-70
      Volume 6 ml/kg with PL >25 or PIP >25
      Adequate PEEP
  FiO2>60 after surfactant
  Any newborn <25 weeks

## Slide 91: High frequency ventilation
Volume:
Same principles as in CMV
Starting volume = 2 mL/kg
      May require a larger volume
      Adjust according to PCO2
Parameters
Notes: DOVE trial
Même raisonnement qu’en conventionnel, il est normal que les bébés les plus petits aient besoin d’un volume plus grand vu l’espace mort

## Slide 92: High frequency ventilation
Average pressure:
Consideration
      Change for PCO2 vs FiO2
        Any MAP increase of ≥2 requires an RXP
        OR
        Any increase in MAP that does not lead to improvement
Parameters
Notes: Si changement pour FiO2 : MAP = MAP en conventionnel +2
Si changement pour PCO2 : MAP = MAP en conventionnel
Toute augmentation de MAP nécessite un RXP

## Slide 93: High frequency ventilation
Hz:
10 Hz:
      Do not change the Hz, the VN500 is not powerful enough to be effective with Hz >10
I:E:
Should be 1:2 (33%)
      Limits air-trapping
Parameters
Notes: Études d’australie : Tingay : perte de puissance sur la méthode de créer la VHF, Piston versus valves + tubulure rigide

## Slide 94
Situation:
I'm calling because BB S continues to deteriorate in HFF on the VN500

## Slide 95: VN500
Tingay, D. G. et al. Are All Oscillators Created Equal? In vitro Performance Characteristics of Eight High-Frequency Oscillatory Ventilators. Neonatology 108, 220–228 (2015).
Notes: Amplitude vs amplitude mesurée
Symboles ouverts tube 2.5
Symboles fermés tube 3.5
5 hz cercles
10 Hz carrés
15 Hz Losanges

## Slide 96: VN500
Tingay, D. G. et al. Are All Oscillators Created Equal? In vitro Performance Characteristics of Eight High-Frequency Oscillatory Ventilators. Neonatology 108, 220–228 (2015).
Notes: Relationship between frequency and ΔPTRACH (black circles) and VT at the airway opening (open diamonds) at a maximum ΔPVENT or ΔPVENT closest to 50 cm H2O (Sophie and BL8000), CL of 1.0 ml/cm H2O, PAW of 10 cm H2O and a 2.5-mm ETT. Data at a 1:2 I:E ratio (a) and 1:1 I:E ratio (b).
* Unable to generate ΔPVENT >45 cm H2O at 15 Hz (VN500) or all frequencies (BL8000).

## Slide 97: Vn500
Grazioli, S., Karam, O. & Rimensberger, P. C. New Generation Neonatal High Frequency Ventilators: Effect of Oscillatory Frequency and Working Principles on Performance. Respir Care 60, 363–370 (2015).
Notes: A: modèle enfant à terme
B: Modèle enfant prématuré
M15 et I:E 1:1
Max à 10hz = 55
Max à 15hz = 33

## Slide 98: vn500
Grazioli, S., Karam, O. & Rimensberger, P. C. New Generation Neonatal High Frequency Ventilators: Effect of Oscillatory Frequency and Working Principles on Performance. Respir Care 60, 363–370 (2015).
Notes: A: Full term infant setting for the test – Cible 4 mL
B: preterm infant settings for the test – Cible 1 mL
Mean à 15
I:E 1:1
Amplitude Max non limitée
Bleu : Modèle normal
Triangle orange: Modèle restrictif
Losanges verts: Modèle obstructif
Carrés noirs: modèle mixte

## Slide 99
Optimization of HFF on the VN500

## Slide 100
Situation:
I changed BB S to amplitude because it wasn't working in volume

## Slide 101
What questions to ask?

## Slide 102: Amplitude vs Volume
VG
Amplitude
Notes: Pourquoi ça a « fonctionné » en amplitude?

## Slide 103
extubation

## Slide 104: Spontaneous breathing test
Who: Patients <1250g
What: CPAP ET x 3 minutes
Failure if:
      Bradycardia
      Desaturation <85% despite 15% increase in FiO2
      Increase of >15% FiO2
Apnea ≠ Failure

## Slide 105: Spontaneous breathing test
Kamlin, C. O. F., Davis, P. G., Argus, B., Mills, B. & Morley, C. J. A trial of spontaneous breathing to determine the readiness for extubation in very low birth weight infants: a prospective evaluation. Arch. Dis. Child. - Fetal Neonatal Ed. 93, F305 (2008).
Kamlin, C. O. F., Davis, P. G. & Morley, C. J. Predicting successful extubation of very low birthweight infants. Archives of Disease in Childhood - Fetal and Neonatal Edition 91, F180-3 (2006).
Notes: Comparaison entre
VM
TRS
Ration VM
TRS:
Extubation + précoce
Souvent à des paramètres plus élevés

## Slide 106: Spontaneous breathing test
Comment:
    CPAP ET (VS-PEP) without Ai and without apnea ventilation
    If HFF:
      MAP > 12 : PEEP +8
      MAP ≤ 12 : PEEP + 6-7

## Slide 107: Invasive ventilation
D: Displaced
O: Obstructed
P: Pneumothorax
E: Equipment

## Slide 108: QUESTIONS?